## Slide 1: QST
details

## Slide 2: Capabilities
Extend to 30 inches
Speed of 24 in/sec
force of 10,000 lbs
Break detection
Accuracy within 5-100ths of an inch
Optional 4 triaxial accelerometer mounted bed plate
2 axis positioning
Vertical or horizontal piston positioning

## Slide 3: Components
Analog out Krypton module +- 10v DC
Load Cell 10K LBS Compression
MBR-V200 monitor Vout
String pot to measure Position
ATOS electrohydraulic two way proportional valve

## Slide 4: Sequencing
Program to set up parameters for QST stand to run.
Run a single force push test to a position hold and return to zero position.
Custom sequences reusable through out program. ie.( homing sequence)
Monitoring
  Pressure
  Position
  Force
Safety precautions
  Pre-check/setup
    pressure Check
    Position check
    speed check
  Arm timeout
  PID controlled Position

## Slide 5: Questions
Changing a PID max and MIN value using sequencer